## Slide 1
8-bit Arithmetic Logic Unit
Proiect — Calculatoare Numerice
Ștefănescu Alexandru Ștefan | Varga Andreea Florina
Trifuț Alexandra Rebecca | Șulan Stanko

## Slide 2
1. Project Overview and Objectives
Proiectarea si implementarea unui ALU pe 8 biti capabil sa execute adunare, scadere, inmultire (Booth Radix-2) si impartire (Restoring Division), coordonat de o unitate de control FSM implementata structural in Verilog.
F
Functionalitate
Implementarea corecta a operatiilor aritmetice cu circuite logice eficiente
S
Structura
Ierarhie clara — module separate pentru fiecare operatie si modul de control
V
Validare
Testbench complet pentru verificarea rezultatelor si generare waveforms
P
Performanta
Timp de propagare minim si utilizare eficienta a resurselor hardware

## Slide 3
2. Architecture — Module Principale
Datapath — Stocare si Deplasare
Reg A — Accumulator 8-bit
Reg B — Operand B 8-bit
Reg M — Multiplicand/Divisor
Reg Q — Multiplier/Dividend
Q-1 FF — 1-bit flip-flop
DSR Shift Logic — Arith. Shift Right
Counter 3-bit — 8 iteratii
Blocuri Aritmetice si Control
Full Adder 1-bit (structural)
Adder/Subtractor 8b — 8x FA + XOR
MUX 2:1 x 8bit — ASU.A si Mux B
ASU Mux — selectie ADD/SUB
Booth Mult — Booth Radix-2
Restoring Div — Restoring Division
Control Unit — FSM 6 stari

## Slide 4
2.3 FSM — Control Unit

## Slide 5
2.4 Diagrama Hardware

## Slide 6
3. Algorithm Functionalities
Booth Radix-2 — Inmultire
1. Initializare: A=0, M=multiplicand, Q=multiplier, Q[-1]=0
2. Evalueaza {Q[0], Q[-1]}:
01 → A = A + M
10 → A = A - M
00/11 → nicio operatie
3. Arithmetic Shift Right {A, Q, Q[-1]}
4. Repeta 8 iteratii
5. Rezultat 16-bit = {A[7:0], Q[7:0]}
Restoring Division — Impartire
1. Initializare: A=0, Q=dividend, M=divisor
2. Shift stanga {A, Q} cu 1 bit
3. A_new = A - M
4. Daca A_new >= 0: A=A_new, Q[0]=1
5. Daca A_new < 0: restore A, Q[0]=0
6. Repeta 8 iteratii
7. Q = Cat, A = Rest
8. div_by_zero daca M=0

## Slide 7
4. HDL Implementation — Module Verilog
Fisier
Descriere
full_adder.v
Full Adder 1-bit (XOR, AND, OR)
adder_subtractor_8b.v
8x FA + XOR pentru SUB
mux_2to1_8b.v
Multiplexor 2:1 pe 8 biti
asu_mux.v
Selectie ADD/SUB (ASU Mux)
reg_8b.v / reg_1b.v
Registre 8-bit si 1-bit
dsr_shift.v
Arithmetic Shift Right A:Q
counter_3b.v
Counter 3-bit (8 iteratii)
booth_mult.v
Inmultire Booth Radix-2
restoring_div.v
Impartire Restoring Division
control_unit.v
FSM Control Unit — 6 stari
alu_8bit.v
Top-Level — integreaza totul
tb_alu_8bit.v
Testbench — 14 teste

## Slide 8
4.2 OpCodes & Ierarhia Modulelor
OpCodes
00
Adunare (ADD)
01
Scadere (SUB)
10
Inmultire — Booth Radix-2
11
Impartire — Restoring Division
Ierarhia Modulelor
alu_8bit (Top-Level)
control_unit — FSM 6 stari
mux_2to1_8b (x2) — ASU.A Mux, Mux B
asu_mux — selectie ADD/SUB
adder_subtractor_8b — 8x full_adder
reg_8b (x2) — Reg A, Reg B
booth_mult — Booth Radix-2
restoring_div — Restoring Division

## Slide 9
5. Testing and Simulation Results
14 PASS / 0 FAIL
Op
Test
Rezultat (hex)
Status
ADD
15+27=42
002A
PASS
ADD
0+0=0
0000
PASS
ADD
100+55=155
009B
PASS
SUB
50-20=30
001E
PASS
SUB
10-10=0
0000
PASS
SUB
10-30=-20
FFE6
PASS
MUL
6x7=42
002A
PASS
MUL
0x255=0
0000
PASS
MUL
-4x3=-12
FFF4
PASS
MUL
15x15=225
00E1
PASS
DIV
42/6=7 r0
Q=07
PASS
DIV
17/5=3 r2
Q=03
PASS
DIV
100/10=10
Q=0A
PASS
DIV
10/0
div_by_zero=1
PASS
Waveforms vizualizate in GTKWave — fisier tb_alu_8bit.vcd

## Slide 10
6. Bibliografie si Tool-uri
Bibliografie
Oprițoiu Flavius (2026) — Arhitectura Calculatoarelor, Universitatea Politehnica
Patterson, D., Hennessy, J. — Computer Organization and Design
Weste, N., Harris, D. — CMOS VLSI Design
Tool-uri folosite
Icarus Verilog (iverilog) — compilare si simulare cod Verilog
GTKWave — vizualizare waveforms (.vcd)
Visual Studio Code — editare cod HDL
ALU 8-bit • Arhitectura Calculatoarelor • 2025-2026